## Slide 1
Hypernetwork-Driven Test-Time Adaptation
for WiFi Indoor Localization
Architecture
Base network: a simple MLP, trained once offline, frozen forever
Hypernetwork reads statistics of a rolling buffer of UNLABELED fingerprints
It predicts a weight correction for the base network's FINAL LAYER only
No ground-truth labels are ever used at deployment time

## Slide 2
UJIIndoorLoc Pipeline
Baseline 10.80m -> found a real floor-conflation bug (floors share near-identical footprints) -> fixed with a floor classifier -> 8.05m
Hypernetwork design,
Result: 13.60m → 13.37m under drift (~1.7% relative improvement)
Diagnosed as sparsity-limited: only 3.8% of 520 APs visible per fingerprint

## Slide 3
Dataset Switch
Candidate denser datasets, compared directly on AP visibility and split feasibility:
Dataset | Total APs | Visible % | Floors | Groups | Verdict
UJIIndoorLoc (current) | 520 | 3.8% | 5 (merged) | 12 / 4 | baseline
SOD-HCXY | 56 | 22.3% | 1 | 8 | CHOSEN
SOD-SYL | 46 | 38.8% | 1 | 3 | too few groups
SOD-CETC331 | 52 | 49.4% | 3 | 1 | no grouping
Why SOD-HCXY
~6x denser AP visibility than UJIIndoorLoc -- directly tests the sparsity hypothesis
Single floor -- sidesteps the floor-conflation problem entirely
Same UserID/PhoneID grouping metadata, so the same leakage-free split methodology applies
Official train/test split verified to have ZERO overlapping reference points

## Slide 4
SOD-HCXY Results
Clean baseline: 8.47m mean / 3.98m median error
Robust headline result -- averaged across 15 independent random drift realizations
11.66m ± 0.29m
Frozen
10.78m ± 0.19m
Adapted
+0.88m (7.6%)
Improvement
15 / 15 seeds: adapted beat frozen

## Slide 5
SOD-HCXY Results
Clean baseline: 8.47m mean / 3.98m median error
Robust headline result -- averaged across 15 independent random drift realizations
11.66m ± 0.29m
Frozen
10.78m ± 0.19m
Adapted
+0.88m (7.6%)
Improvement
15 / 15 seeds: adapted beat frozen
Verified real, not trivial shrinkage: correction magnitude tracks the TRUE hidden drift severity, growing within a session and resetting at each new session boundary
Tried more complexity (trunk-level correction, not just the head) -- flat-to-slightly-worse (7.4% vs 8.5%); reverted to the simpler head-only mechanism

## Slide 6
Conclusions
 | UJIIndoorLoc | SOD-HCXY
Total APs | 520 | 56
AP visibility | 3.8% | 22.3%
Clean baseline | 8.05m | 8.47m
Frozen -> adapted | 13.60m -> 13.37m | 11.66m -> 10.78m
Relative improvement | 1.7% | 7.6-8.5%
Robustness | single realization | 15/15 seeds positive
Key takeaway: Sparse RSSI → weak TTA effect. Dense RSSI → real, robust TTA effect.
This comparison -- not either number alone -- is the cleanest finding: AP density determines whether buffer-statistics-driven test-time adaptation can separate “location” from “drift.”